## Slide 1
Cantilever-based microscopy in biophysics
Clementine Fournier
November 15, 2016
Image Credit: Muller et al. (2008)

## Slide 2
2
Outline
Cantilever-based microscopy in biophysics
I. Operating principles of an Atomic Force Microscope (AFM)
II. Two possible uses: high resolution imaging and nano-force testing
III. Applications in biophysics

## Slide 3
3
Outline
Cantilever-based microscopy in biophysics
I. Operating principles of an Atomic Force Microscope (AFM)
II. Two possible uses: high resolution imaging and nano-force testing
III. Applications in biophysics

## Slide 4
4
Operating principles of an Atomic Force Microscope (AFM)
How does an AFM work?
Image Credit: Department of Materials, ETH Zurich
Image Credit: Physics Department, Warwick University

## Slide 5
5
Operating principles of an Atomic Force Microscope (AFM)
How does an AFM work?
Operating principle? Interaction between the atom on the edge of the tip and the sample’s atoms
Signal measured? Deflection of the cantilever upon tip-sample interaction
Force resolution? A few piconewtons
Operating conditions? In air or liquid environments
At every temperature around ambient

## Slide 6
6
Operating principles of an Atomic Force Microscope (AFM)
What kind of samples for this technique?
Image Credit: Princeton University, Sarah Pfau
AFM = Ideal for in vitro biological applications
Samples range from single molecule to entire cell
Image Credit: De Oteyza et al. (2013)
Image Credit: Fairman studio LLC

## Slide 7
7
Outline
Cantilever-based microscopy in biophysics
I. Operating principles of an Atomic Force Microscope (AFM)
II. Two possible uses: high resolution imaging and nano-force testing
III. Applications in biophysics

## Slide 8
8
Two possible uses: high resolution imaging and nano-force testing
High resolution imaging
AFM: topography recorder
Result: 3D mapping of a sample
and height profile
Resolution: nano-scale
more recently angstrom-scale
Image Credit:
De Oteyza et al.
(2013)
Image Credit:
Muller et al.
(2007)

## Slide 9
9
Two possible uses: high resolution imaging and nano-force testing
Force spectroscopy
Image Credit: Galajda et al. (2015)
AFM: nanomechanical tester
Possible applications:
Friction measurement, micro-
lithography, acquisition of
force-distance curves.
Example: Vinckier, Semenza (1998)
Young’s modulus calculation for cells
or microtubules.

## Slide 10
10
Outline
Cantilever-based microscopy in biophysics
I. Operating principles of an Atomic Force Microscope (AFM)
II. Two possible uses: high resolution imaging and nano-force testing
III. Applications in biophysics

## Slide 11
11
Applications in biophysics
From single molecules to cells mapping
Image Credit: Muller et al. (2007)
One example : Muller et al. (2008)
Observation of native membrane proteins at work
Picture: Communication channels from rat liver cells. Gap junctions closing due to pH change.

## Slide 12
12
Applications in biophysics
From single molecules to cells mapping
Another example: Light-driven proton pump bacteriorhodopsin (BR)
Removal of one BR : global rearrangements
Image Credit: Muller et al. (2007)

## Slide 13
13
Applications in biophysics
Cantilever-based biosensors
Receptor-ligand binding tester
Example: Florin et al. (1994)
Image Credit: Florin et al. (1994)
Finding the receptor-ligand unbinding force between biotin and avidin using a force-displacement curve
Using bio-recognition

## Slide 14
14
Applications in biophysics
Cantilever-based biosensors
Image Credit: Phillips et al., Physical biology of the cell, Garland Science
Biofunctionalized cantilevers: similar to the AFM. Binding of molecules to the surface alters the surface free energy
Ligands

## Slide 15
15
Applications in biophysics
Cantilever-based biosensors
Image Credit: Fritz et al. (2000)
Example : Fritz et al. (2000) Monitoring single strand DNA hybridization with two microcantilevers in parallel
System able to detect a single base mismatch

## Slide 16
16
Applications in biophysics
But also…
Image Credit: Liu et al. (2010)
Cellular biomechanics
Cell-cell interactions
…

## Slide 17
References
De Oteyza DG, Gorman P, Chen YC, Wickenburg S, Riss A,
Mowbray DJ, Etkin G, Pedramrazi Z, Tsai HZ, Rubio A,
Crommie MF, Fischer FR (2013) Science 340:1434-1437.
Muller DJ, Engel A, (2007) Curr Opin Colloid Interface Sci
Vinckier A, Semenza G (1998) FEBS Lett 430:12-16.
Florin EL, Moy VT, Gaub HE (1994). Science 264:415-
417.
J. Fritz, M.K. Baller, H.P. Lang, H. Rothuizen, P. Vettiger, E.
Meyer, H.-J. Güntherodt, C. Gerber, J.K. Gimzewski, (2000)
Science 288 316–318.
Liu Y, Pinzon-Arango PA, Gallardo-Moreno AM, Camesano
TA (2010) Mol Nutr Food Res 54:1744-1752.
Image Credit: Muller et al. (2007)

## Slide 18
Thank you!
Questions?
Image Credit: Muller et al. (2007)